ΘΨ- position( angle) of rotor flux space-vector( TODO(ref)freescale)
ωe, ωs, ωmr - electrical angular frequency, angular speef of the rotor-flux-oriented reference frame
ωr - electrical velocity rotor (np*ω)

ωsl - velocity slip (ωs- ωr )

Idn- Idn : rated d-axis stator current (2012 Melo et all, pag.405)

Vmax- Vmax

Imax- Imax
: motor (or inverter) voltage and current limits, respectively; (2012 Melo et all, pag.405)

Imin- corrente mínima correspondente à corrente de magnetização?(AMRC)

wn- ωn: rated speed (2012 Melo et all, pag.406)

wc- ωc: boundary speed between constant power and power-speed; (2012 Melo et all, pag.407)	(limite entre zona 2 e zona 3)

np- numero de pares de polos

M- Indutância de magnetização

Lr- rotor total inductance

Kt	3/2*np*M*M/Lr

Tm1- Torque máximo na região 1; (2012 Melo et all, pag.407)

Rm- equivalent stator iron losses resistances; (2012 Melo et all, pag.404)

Llr- Llr: rotor leakage inductance; (2012 Melo et all, pag.404)

velocity controller:
vel_p- pg_:	//proportional gain (tpid_class.h)

vel_Min_pid_res	// minimum setpoint (tpid_class.h)

vel_Max_pid_res	// maximum setpoint (tpid_class.h)

vel_cel-	// Acceleration limit (rate of change) (tpid_class.h)

torque controller:
(...)
torque_control_i- ig_;	// integral gain (tpid_class.h)
(…)

current_control_y- poderia se escrever current_control_q; (y é o mesmo que q)

(o mesmo que o anterior para x e d)

Θ_Ψ= int from {0} to {t} left ( { ω_r+ω_sl } right ) { dt }

U_sd = R_s i_sd + {partial %PSI _sd} over { partial t} - %omega_s %PSI_sq	(1)
U_sq = R_s i_sq +{partial %PSI _sq} over { partial t} - %omega_s %PSI_sd	(2)
U_rd = 0 = R_r I_rd + {partial %PSI _rd} over { partial t} - (%omega_s - %omega_r) %PSI_rq	(3)
U_rq = 0 = R_r I_rq + {partial %PSI _rq} over { partial t} + (%omega_s - %omega_r) %PSI_rd	(4)
%PSI_sd = L_s I_sd + L_m I_rd	(5)
%PSI_sq = L_s I_sq + L_m I_rq	(6)
%PSI_rd = L_r I_rd + L_m I_sd	(7)
%PSI_rq = L_r I_rq + L_m I_sq	(8)

T_e = {3} over {2} P_p (%PSI_sd I_sq - %PSI_sq I_sd)	(9)

=>
I_rd = (%PSI_rd - L_m I_sd)/L_r	(10)
I_rq = (%PSI_rq - L_m I_sq)/L_r	(11)

{partial %PSI _rd} over { partial t} = 1/T_r( -%PSI_rd + L_m I_sd)+ (%omega_s - %omega_r) %PSI_rq (12)
{partial %PSI _rq} over { partial t} = 1/T_r( -%PSI_rq + L_m I_sq)- (%omega_s - %omega_r) %PSI_rd	(13)

We assume the rotor rotor flux space-vector is aligned to the to the d-axis of the rotating reference frame:

%PSI_rd = lline bar %PSI_r rline	(14)
qqqq and
%PSI_rq = 0	(15)

{partial (bar %PSI _r)} over { partial t} = ( L_m I_sd)/T_r - bar %PSI_r/T_R	(16)

bar I_mr = bar %PSI_r / L_m	(17)
L_m {partial I_mr } over { partial t} = ( L_m I_sd)/T_r - (L_m I_mr) /T_r = ( I_sd - I_mr )/T_r <

(4) e (8) e (14) e (15) e (17) :

(%omega_s - %omega_r) bar I_mr L_m = 1/Tr L_m I_sq
(%omega_s - %omega_r) = 1/T_R I_sq/( bar I_mr) <

: I_mr ^k = I_mr ^( k-1 ) + T_s/Tr( I_sd ^k - I_mr ^( k-1 ) )
: %THETA _ %PSI ^k = %THETA _ %PSI ^(k-1) + T_s ( %omega_r ^k +1/T_r I_sq ^k /I_mr ^k )

Velocidade sempre em medida eléctrica, somente quando se quer saber mecânica é que se divide por numero par de pólos

Porquê o circuito de decouple?
Porque Ud não é somente proporcional a Id mas tb de Iq
Idem para Uq
Para além disto há tb a componente de atraso

BIBLIOGRAFIA

Lim, S. and K. Nam (2004). Loss-minimising control scheme for induction motors. IEE
Proceedings - Electric Power Applications, Vol.151, No.4

Pedro Melo, Ricardo de Castro and Rui Esteves Araújo. Evaluation of an Energy Loss-Minimization Algorithm for EVs Based on Induction Motor,- Intech

Levi, E.: ‘Impact of iron loss on behavior of vector controlled
induction machines’, IEEE Trans. Ind. Appl., 1995, 31, (6), pp.1287–1296

Novotny, D.W., and Lipo, T.A.: ‘Vector control and dynamics of AC
drives’, (Clarendon Press, Oxford, UK, 1996)

Zbigniew Gmyrek, Aldo Boglietti and Andrea Cavagnino;Estimation of Iron Losses in Induction Motors: Calculation Method, Results, and Analysis;IEEE

Sinisa Jurkovic INDUCTION MOTOR * PARAMETERS EXTRACTION; MIT

Vas P., Sensorless Vector and Direct Torque Control, Oxford University Press, ISBN
0-19-856465-1, New York, 1998

3-Phase AC Induction Vector Control Drive with Single Shunt Current Sensing;Designer Reference Manual;DRM092 Rev. 0 7/2007, freescale.com

Anno Yoo LSIS Co., Ltd., Anyang, Korea;Robust On-line Rotor Time Constant Estimation for
Induction Machines;Journal of Power Electronics, Vol. 14, No. 5, pp. 1000-1007, September 2014;http://dx.doi.org/10.6113/JPE.2014.14.5.1000
ISSN(Print): 1598-2092 / ISSN(Online): 2093-4718

Torque Transmissibility Assessment for Automotive Dry-Clutch Engagement;
https://www.researchgate.net/publication/224135585